## Slide 1: Analytical and Regulatory Issues Surrounding U.S. Nuclear Performance Standards (NPS)
George L. Fitzpatrick
August 28, 2012

## Slide 2: George Fitzpatrick’s Relevant Experience
US Nuclear Performance Standard analytical and expert witness experience:
  Palo Verde 1,2,3 (Texas, New Mexico, California and Arizona)
  Comanche Peak 1 and 2 (Texas)
  Indian Point 2&3 (New York)
  Wolf Creek (Kansas and Missouri)
  Plant Vogtle (Georgia)
  Plant Hatch (Georgia)
  Shoreham (New York)
  San Onofre 2&3 (California)

## Slide 3: Historical U.S. State Regulatory Focus On Nuclear Generation
Safety
Security
Capacity Factors
Forced Outages
Refueling Outage Cost and Durations
Operation & Maintenance Costs
Capital Additions Costs
These inquiries were usually initiated by a particular event or specific cost reviews as part of a rate case. They were not part of an automated regulation process.

## Slide 4: An Overriding US NRC Concern- Effects of Performance Standards on Safety
On July 24, 1991, the U.S. Nuclear Regulatory Commission (NRC) expressed its safety-related concerns if state commissions imposed Nuclear Performance Standards (NPS) on its Licensees. The following points were stressed:
  Certain forms of economic performance incentives may adversely affect the operation of nuclear plants and public health and safety;
  Certain methods of measuring nuclear performance are of particular concern (e.g., use of sharp thresholds, short time interval measurements, lack of “null zones”, and reliance on SALP (Systematic Assessment of Licensee Performance) scores);
  NRC will continue to monitor state commission activity in this area
  NRC urges that licensees and regulatory commissions inform the NRC of NPS programs that are being considered for application to NRC licensees

## Slide 5: Nuclear Performance Observations
US nuclear units that I have statistically modeled go through an non-linear maturing process. As units progress toward the end of their lifecycle, Capacity Factor is likely to decline and Operation & Maintenance Costs may increase (significant management effort/ initiatives would be required to reverse this trend)
Using industry averages to set targets for performance for individual nuclear units is a statistically inferior approach. Informed averages, or model-based “most likely performance” estimators are better statistical measurement methods
In the case of U.S. Pressurized Water Reactors, for example, there are 11 statistically significant variables that have either a positive or negative effect on Capacity Factor. These factors would likely affect CANDU unit performance as well.
“Extraordinary Events” should also be identified and agreed to in advance of an NPS and then be excluded from any model-based performance calculation. Based on my experience, this process involves lengthy discussion over many months.

## Slide 6: Examples of Statistically Significant Factors Affecting U.S. PWR Nuclear Unit Performance
Maturing operating age (non-linear variable structures track plateauing then declining capacity factor)
Immature operating age (e.g., less than 6 years from Commercial Operation Date)
Cooling Water type
Cooling Tower type
Containment type
Reactor system type

## Slide 7: Examples of Statistically Significant Factors Affecting U.S. PWR Nuclear Unit Performance
Steam Generator type
Steam Generator Replacement completed
Reactor Vessel Head Replacement completed
Commercial Operating Date (the older the vintage, the lower the performance)
Fleet vs. Non Fleet units

## Slide 8: Conclusions Based Upon My U.S. Nuclear Performance Modeling and Regulatory Experience
Nuclear unit performance follows an “S” shaped trajectory that shows Capacity Factor increasing to its mid-life and then plateauing and declining as it reaches the end of its lifecycle
The earlier the design and Commercial Operating Date, the lower the expected lifecycle capacity factor, all else equal
The challenge for nuclear plant management: get the best performance from aging nuclear assets while maintaining the highest level of safety

## Slide 9: Conclusions Based Upon My U.S. Nuclear Performance Modeling and Regulatory Experience
Key question for regulators: Will the imposition of an NPS cause plant management to operate any differently? My interactions with a representative sample of U.S. nuclear plant management indicates they will always strive for excellence in both safety and performance. Based on my U.S. experience, incentives (penalties) tied to performance standards would not change nuclear performance
The vast majority of US state commissions that I have worked with have reached that same conclusion

## Slide 10: Conclusions Based Upon My U.S. Nuclear Performance Modeling and Regulatory Experience
Many U.S. commissions opt for frequent communications on costs and performance between commission staff and nuclear personnel
According to the NRC, Nuclear Performance Standards can have unintended consequences that could affect decision making and safety
According to the nuclear plant senior management personnel with whom I have worked, Nuclear Performance Standards can have unintended consequences that could affect employee morale and ultimately the retention of qualified experts and proven senior management