## Slide 1: Activity and Program-based Benchmarking (APB)
Stakeholder Consultation
EB-2018-0278
November 30, 2022

## Slide 2: Land Acknowledgement
The Ontario Energy Board acknowledges that our headquarters in Toronto is located on the traditional territory of many nations including the Mississaugas of the Credit, the Anishnabeg, the Chippewa, the Haudenosaunee and the Wendat peoples. This area is now home to many diverse First Nations, Inuit and Métis peoples. We also acknowledge that Toronto is covered by Treaty 13 with the Mississaugas of the Credit.
We are grateful for the opportunity to gather and work on this land and recognize our shared responsibility to support and be good stewards of it.

## Slide 3: Stakeholder Meeting Objectives
Recent Highlights
Review 2021 unit cost results
Discuss potential improvements to unit cost metrics
Gather feedback on APB initiative

## Slide 4: OEB Business Plan
EVOLVE TOWARDS BECOMING A TOP QUARTILE REGULATOR
DRIVE ENERGY SECTOR PERFORMANCE
Further refine the approach to benchmarking to support its increased value in the rate-setting process RRR review and opportunities for improvement
Implement OEB program-level benchmarking
Develop Workplan |  |  | 
Q1
Q2
Q3
Q4
 | Next APB report | Engage on refinement to APB | Implement new APB models
Q1
Q2
Q3
Q4
2022/23 Business Plan Actions

## Slide 5: Recent Highlights

## Slide 6: Engage with Us Page
APB Engage with Us Page – Link
Purpose of the page
  Stakeholder engagement
  Stakeholder feedback

## Slide 7: Unit Cost Report (1)
5-Year trend of
Input Variables

## Slide 8: Unit Cost Report (2)
Unit Cost Formula
5-Year Trend of
Industry Aggregate Unit Cost

## Slide 9: Unit Cost Report (3)
Unit Cost
Histogram
for Latest Year

## Slide 10: 2021 Unit Cost Results, Stakeholder Feedback, & Potential Improvements

## Slide 11: Q: In your opinion, which of the following 10 O&M and CapEx programs should be enhanced in the near term?
Program | Number of Responses
Distribution station equipment CapEx | 6
Distribution station equipment O&M | 5
Line transformers CapEx | 5
Vegetation management O&M | 3
Meters CapEx | 3
Meters O&M | 2
Poles, towers and fixtures CapEx | 3
Poles, towers and fixtures O&M | 3
Billing O&M | 3
Lines O&M | 1

## Slide 12: General Feedback
Reporting inconsistencies between the distributors data could make distributor to distributor comparison less effective
Capital expenditure corresponding to enhancement of the existing equipment or re-use of the equipment on another site
Annual detailed reporting by distributors on variances if the benchmark is exceeded
Annual survey would be valuable

## Slide 13: Distribution Station Equipment CapEx
Chart: Industry Aggregate Distribution Station Equipment Capex Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Unit Cost | 9398663.7174 | 6546623.7234 | 6920452.7802 | 2736375.8427 | 3579754.6203
Chart: 2021 Distribution Station Equipment O&M Unit Costs
| 0 - 5000 | 5000 - 10000 | 10000 - 15000 | 15000 - 20000 | 20000 - 25000 | 25000 - 30000 | 30000 - 35000 | 35000 - 40000 | 40000 - 45000 | 45000 - 50000 | 50000 - 55000 | 55000 - 60000 | 60000 - 65000 | 65000 - 70000 | > 70000
Series 1 | 7 | 7 | 2 | 3 | 0 | 1 | 2 | 0 | 1 | 0 | 2 | 0 | 1 | 0 | 8

## Slide 14: Distribution Station Equipment CapEx
Survey Results
Question: What enhancement opportunities do you see?
Responses:
Total MVA in the denominator is normalized using total number of stations but the numerator is not normalized.
Metric does not account for differences in configurations, age demographics or asset conditions.
Discussion: What steps could be taken to enhance this unit cost metric?

## Slide 15: Distribution Station Equipment CapEx
Potential Improvements
New Formula:

## Slide 16: Distribution Station Equipment CapEx
Chart: Industry Aggregate Distribution Station Equipment Capex Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Unit Cost | 1632.503 | 1178.4843 | 1315.3076 | 447.2787 | 1078.7384
Chart: 2021 Distribution Station Equipment O&M Unit Costs
| 0 - 500 | 500 - 1000 | 1000 - 1500 | 1500 - 2000 | 2000 - 2500 | 2500 - 3000 | 3000 - 3500 | 3500 - 4000 | 4000 - 4500 | 4500 - 5000 | 5000 - 5500 | 5500 - 6000 | 6000 - 6500 | 6500 - 7000 | 7000 - 7500 | > 7500
Series 1 | 20 | 5 | 2 | 2 | 3 | 1 | 2 | 1 | 0 | 2 | 2 | 1 | 1 | 0 | 2 | 1
New Formula:

## Slide 17: Distribution Station Equipment O&M
Chart: Industry Aggregate Distribution Station Equipment O&M Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Unit Cost | 3079159.211 | 2586073.8671 | 2529346.8325 | 2636951.7098 | 2864104.2509
Chart: 2021 Distribution Station Equipment O&M Unit Costs
| 0 - 5000 | 5000 - 10000 | 10000 - 15000 | 15000 - 20000 | 20000 - 25000 | 25000 - 30000 | 30000 - 35000 | 35000 - 40000 | 40000 - 45000 | 45000 - 50000 | 50000 - 55000 | 55000 - 60000 | 60000 - 65000 | 65000 - 70000 | > 70000
Series 1 | 7 | 8 | 8 | 4 | 1 | 2 | 2 | 0 | 2 | 0 | 1 | 3 | 1 | 0 | 5

## Slide 18: Distribution Station Equipment O&M
Survey Results
Question: What enhancement opportunities do you see?
Responses:
Does not account for differences in configurations
Does not account for age demographics or asset condition
Total MVA in the denominator normalized using total number of stations but the numerator is not normalized.
Discussion: What steps could be taken to enhance this unit cost metric?

## Slide 19: Distribution Station Equipment O&M
Potential Improvements
New Formula:

## Slide 20: Distribution Station Equipment O&M
Chart: Industry Aggregate Distribution Station Equipment O&M Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Unit Cost | 1166.2468 | 983.0035 | 957.6043 | 935.56 | 1051.2612
Chart: 2021 Distribution Station Equipment O&M Unit Costs
| 0 - 500 | 500 - 1000 | 1000 - 1500 | 1500 - 2000 | 2000 - 2500 | 2500 - 3000 | 3000 - 3500 | 3500 - 4000 | 4000 - 4500 | 4500 - 5000 | 5000 - 5500 | 5500 - 6000 | 6000 - 6500 | 6500 - 7000 | > 7000
Series 1 | 6 | 11 | 10 | 7 | 3 | 3 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 2
New Formula:

## Slide 21: Vegetation Management O&M
Chart: Industry Aggregate Vegetation Management O&M Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Billing O&M | 64.0675 | 66.0895 | 74.8028 | 65.5655 | 68.4629
Chart: 2021 Vegetation Management O&M Unit Costs
| 0 - 5 | 5 - 10 | 10 - 15 | 15 - 20 | 20 - 25 | 25 - 30 | 30 - 35 | 35 - 40 | 40 - 45 | 45 - 50 | 50 - 55 | 55 - 60 | 60 - 65 | 65 - 70
Series 1 | 2 | 1 | 5 | 7 | 5 | 6 | 6 | 6 | 5 | 1 | 1 | 2 | 3 | 2

## Slide 22: Vegetation Management O&M
Survey Results
Question: What enhancement opportunities do you see?
Responses:
Does not account for different tree densities
Question: Vegetation management practices around secondary lines and service wires
Responses:
Secondary Lines* Planned only – 1 distributor Reactive only – 1 distributor Both – 4 distributors None – 1 distributor | Service Wires* Planned only – 1 distributor Reactive only – 3 distributors Both – 2 distributors None – 1 distributor
* 7 Respondents said all expenses are recorded in USoA 5135
Discussion: What steps could be taken to enhance this unit cost metric?

## Slide 23: Vegetation Management O&M
Potential Improvements
Separate reporting of costs related to primary lines.
i.e., USoA 5135 only primary lines and a new USoA for secondary lines/service wires

## Slide 24: Meters CapEx
Chart: Industry Aggregate Meters Capex Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Unit Cost | 17.6472 | 25.5662 | 26.9169 | 10.8379 | 9.3789
Chart: 2021 Meters Capex Unit Costs
| 0 - 2 | 2 - 4 | 4 - 6 | 6 - 8 | 8 - 10 | 10 - 12 | 12 - 14 | 14 - 16 | 16 - 18 | 18 - 20 | 20 - 22 | 22 - 24 | 24 - 26 | 26 - 28 | 28 - 30 | 30 - 32 | 32 - 34 | 34 - 36 | 36 - 38 | 38 - 40 | 40 - 42 | 42 - 44 | 44 - 46 | 46 - 48 | 48 - 50 | > 50
Series 1 | 5 | 9 | 7 | 10 | 4 | 8 | 4 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 25: Meters CapEx
Survey Results
Question: What enhancement opportunities do you see?
Responses:
The metric currently does not account for LDCs that have more large commercial accounts (more expensive to maintain demand meters, CTs & PTs than regular residential meters).
Question: What percentage of meters capex reported in USoA 1860 could be attributed to meters held in reserve?
Responses:
Under 1% – 2 distributors
Approximately 5- 10% – 2 distributors
Between 15-35% – 1 distributor
Hard to measure – 2 distributors

## Slide 26: Meters CapEx
Survey Results
Question: What percentage of the total number of meters capitalized are held in reserve on average in a typical year?
Under 1% – 1 distributor
Approximately 2% – 1 distributor
6.25% – 1 distributor
Between 25-50% – 2 distributors
Discussion: What steps could be taken to enhance this unit cost metric?

## Slide 27: Meters CapEx
Potential Improvements
Additional data reporting on number of meters purchased vs installed in a year
New Formula:

## Slide 28: Meters O&M
* Excludes street lighting, sentinel lighting and Unmetered Scattered Load (USL) connections
Chart: 2021 Metering O&M Unit Costs
| 0 - 5 | 5 - 10 | 10 - 15 | 15 - 20 | 20 - 25 | 25 - 30 | 30 - 35 | 35 - 40 | 40 - 45 | 45 - 50 | 50 - 55 | 55 - 60 | > 60
Series 1 | 4 | 7 | 7 | 15 | 13 | 6 | 1 | 1 | 0 | 0 | 0 | 2 | 1
Chart: Industry Aggregate Metering O&M Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Billing O&M | 14.6986 | 16.1019 | 14.3209 | 12.6681 | 12.7017

## Slide 29: Meters O&M
Survey Results
Question: What enhancement opportunities do you see?
Responses:
The metric currently does not account for LDCs that have more large commercial accounts (more expensive to maintain demand meters, CTs & PTs than regular residential meters).

## Slide 30: Meters O&M
Potential Improvements
Additional data reporting on Total Number of Meters installed in operation (excluding held in reserve)
New Formula:

## Slide 31: Billing O&M
Chart: Industry Aggregate Billing O&M Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Billing O&M | 23.3505 | 23.1465 | 26.5599 | 27.3518 | 26.9736
Trend = ↑ $1.15/Customer/Yr
Chart: 2021 Billing O&M Unit Costs
| 0 - 5 | 5 - 10 | 10 - 15 | 15 - 20 | 20 - 25 | 25 - 30 | 30 - 35 | 35 - 40 | 40 - 45 | 45 - 50 | 50 - 55 | 55 - 60 | > 60
Series 1 | 0 | 0 | 6 | 5 | 13 | 8 | 5 | 2 | 4 | 5 | 0 | 1 | 8
* Excludes street lighting, sentinel lighting and Unmetered Scattered Load (USL) connections

## Slide 32: Billing O&M
Question: What enhancement opportunities do you see?
Responses:
The metric currently does not account for other customer care department functions (e.g., USoA 5320 – Collecting)
Survey Results

## Slide 33: Billing & Collecting O&M
Chart: Industry Aggregate Billing O&M Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Billing O&M | 32.6521 | 31.4769 | 32.7578 | 32.3058 | 31.9452
Trend = Flat
Chart: 2021 Billing O&M Unit Costs
| 0 - 5 | 5 - 10 | 10 - 15 | 15 - 20 | 20 - 25 | 25 - 30 | 30 - 35 | 35 - 40 | 40 - 45 | 45 - 50 | 50 - 55 | 55 - 60 | > 60
Series 1 | 0 | 1 | 1 | 7 | 5 | 2 | 11 | 5 | 1 | 3 | 3 | 5 | 13
* Excludes street lighting, sentinel lighting and Unmetered Scattered Load (USL) connections

## Slide 34: Next Steps
Voting on potential improvements through a survey
Continue publication of annual unit cost report

## Slide 36: Appendix

## Slide 37: Line Transformers CapEx
Chart: Industry Aggregate Line Transformers Capex Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Unit Cost | 14677.4896 | 14895.2179 | 18919.234 | 21888.5652 | 14381.7012
Chart: 2021 Line Transformers Capex Unit Costs
| 0 - 2500 | 2500 - 5000 | 5000 - 7500 | 7500 - 10000 | 10000 - 12500 | 12500 - 15000 | 15000 - 17500 | 17500 - 20000 | 20000 - 22500 | 22500 - 25000 | 25000 - 27500 | 27500 - 30000 | 30000 - 32500 | 32500 - 35000 | 35000 - 37500 | 37500 - 40000 | 40000 - 42500 | 42500 - 45000 | 45000 - 47500 | 47500 - 50000 | 50000 - 52500 | 52500 - 55000 | 55000 - 57500 | 57500 - 60000 | 60000 - 62500 | 62500 - 65000 | > 65000
Series 1 | 5 | 7 | 10 | 12 | 8 | 6 | 5 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0

## Slide 38: Line Transformers CapEx
Survey Results
Question: What enhancement opportunities do you see?
Responses:

## Slide 39: Lines O&M
Chart: Industry Aggregate Lines O&M Unit Costs (2017-2021)
| 2019 | 2020 | 2021
Lines O&M | 1029.9088 | 1044.461 | 1051.9034
Chart: 2021 Lines O&M Unit Costs
| 0 - 250 | 250 - 500 | 500 - 750 | 750 - 1000 | 1000 - 1250 | 1250 - 1500 | 1500 - 1750 | 1750 - 2000 | 2000 - 2250 | 2250 - 2500 | 2500 - 2750 | 2750 - 3000 | 3000 - 3250 | 3250 - 3500 | 3500 - 3750 | 3750 - 4000 | 4000 - 4250 | 4250 - 4500 | 4500 - 4750 | 4750 - 5000 | > 5000
Series 1 | 0 | 1 | 4 | 9 | 7 | 8 | 5 | 4 | 1 | 7 | 0 | 3 | 2 | 3 | 0 | 1 | 0 | 0 | 0 | 2 | 0

## Slide 40: Lines O&M
Survey Results
Question: What enhancement opportunities do you see?
Responses:

## Slide 41: Poles, Towers and Fixtures CapEx
Chart: Industry Aggregate Poles, Towers and Fixtures Capital Expenditure Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Poles, Towers and Fixtures CAPEX | 7158.4876 | 6917.9265 | 8706.3547 | 8976.1624 | 9433.1515
Chart: 2021 Poles, Towers, & Fixtures Capex Unit Costs
| 0 - 2500 | 2500 - 5000 | 5000 - 7500 | 7500 - 10000 | 10000 - 12500 | 12500 - 15000 | 15000 - 17500 | 17500 - 20000 | 20000 - 22500 | 22500 - 25000 | 25000 - 27500 | 27500 - 30000 | 30000 - 32500 | 32500 - 35000 | 35000 - 37500 | 37500 - 40000 | 40000 - 42500 | 42500 - 45000 | 45000 - 47500 | 47500 - 50000 | 50000 - 52500 | 52500 - 55000 | 55000 - 57500 | 57500 - 60000 | 60000 - 62500 | 62500 - 65000 | > 65000
Series 1 | 0 | 10 | 13 | 16 | 5 | 4 | 0 | 1 | 2 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0

## Slide 42: Poles, Towers and Fixtures CapEx
Survey Results
Question: What enhancement opportunities do you see?
Responses:

## Slide 43: Poles, Towers and Fixtures O&M
Chart: Industry Aggregate Poles, Towers and Fixtures O&M Unit Costs (2017-2021)
| 2017 | 2018 | 2019 | 2020 | 2021
Billing O&M | 10.2212 | 10.8779 | 12.2113 | 12.5354 | 12.4379
Chart: 2021 Poles, Towers, & Fixtures O&M Unit Costs
| 0 - 5 | 5 - 10 | 10 - 15 | 15 - 20 | 20 - 25 | 25 - 30 | 30 - 35 | 35 - 40 | 40 - 45 | 45 - 50 | 50 - 55 | 55 - 60 | > 60
Series 1 | 18 | 15 | 14 | 3 | 1 | 3 | 0 | 0 | 0 | 1 | 0 | 0 | 1

## Slide 44: Poles, Towers and Fixtures O&M
Survey Results
Question: What enhancement opportunities do you see?
Responses: